Sistemas de Comunicaciones Digitales

Tarea 1

Luis Fernando Rodriguez Gutierrez	ie705694

Omar Humberto Longoria Gándara

25/01/2020

bits	M
8	256
16	65,536
32	4,294,967,296

bits	SNR / 6.0206*k + 1.7609db
16	98.0905
12	74.0081
8	49.9257
4	25.8433

bits	k*fs bits/s
12	529 200
10	441 000
8	352 800

t = 75min → 4,500 seg
M = 16 bits
fs = 44,100 Hz
fs*M*t = 3,175,200,000 bps
3.175 Gbps

Being Stereo, the result that we got, now is x2

fs*M*t = 6.35 Gbps

FLAC: This one can be used for the desired application. Since it has the requirements for the audio to compress.
MP3:This type of compressor it would be the best to use, since it is one of the most use compressors. But one thing that needs to be aware, its that it would be needed MPEG-2 or MPEG-3. Thus the MPEG-1 does not support 61 bits rate.

Thus considering the applications, the best options would be FLAC for the resolution we can achieve.

M = 2

PAM Signal	Difference

Quantitative Signal

M = 16

PAM Signal	Difference

Quantitative Signal

M = 32

PAM Signal	Difference

Quantitative Signal

M = 128

PAM Signal	Difference

Quantitative Signal

M = 256

PAM Signal	Difference

Quantitative Signal

M = 256

PAM Signal	Difference

Quantitative Signal

Amplitude 5
PAM Signal

Quantitative Signal

Difference

Amplitude 10
PAM Signal

Quantitative Signal

Difference

Amplitude 20
PAM Signal

Quantitative Signal

Difference

bits	k	Px	Pq	SNRdb
16	4	0.5030	0.0017	24.809
12	3.5850	0.5030	0.0026	22.8004
8	3	0.5030	0.0064	18.9831
4	2	0.5030	0.0264	12.8062

Tx
Small section of the signal transmitted via cable.

Rx

The most significant part that I could perceive was that at certain part of the signal it had some noise. Besides that noise and the voltage amplitude lost due to the length of the via to transmit.
By watching the signal for a certain of time I did not notices some difference beside that.